# 基于tilt locking(倾斜锁定)技术的一种锁腔方法

### 论文摘要

基于空间模式的干涉,tilt-locking技术为稳定激光频率或锁定光学谐振腔提供了一种灵活便捷的方法。在本文中,对tilt-locking技术进行了修改并进行了实验演示。该方法使用非谐振的一阶空间模式TEM01模作为相位参考,并利用TEM01模式和TEM00模式的干涉进行光学腔的锁定。在光学腔的反射光路中添加障碍物以阻挡反射光束的一半。反射光束的通过的一半由单像素光电探测器而不是分离探测器来检测,以导出用于将光学腔的TEM00模式谐振频率锁定到激光频率的误差信号。利用此方法可以将光学腔稳定锁定4 h。

### 论文目录

- 0 引言

- 1 实验原理

- 2 实验过程及实验结果

- 3 总结

### 文章来源

类型: 期刊论文

作者: 郝冬冬,翟泽辉,贾鑫,刘志强,郭娟

关键词: 光电探测器,干涉,高阶空间模式,相位基准,障碍物

来源: 量子光学学报 2019年02期

年度: 2019

分类: 基础科学,信息科技

专业: 物理学,无线电电子学

单位: 山西大学物理电子工程学院

基金: 国家重点基础研究发展计划(No.2016YFA0301404),国家自然科学基金重点项目(91536222)

分类号: TN248;TN15

页码: 228-233

总页数: 6

文件大小: 546K

下载量: 33

### 相关论文文献

- [1].Geodetic slip rate and locking depth of east Semangko Fault derived from GPS measurement[J]. Geodesy and Geodynamics 2020(03)

- [2].Decaying evolution dynamics of double-pulse mode-locking[J]. Photonics Research 2018(08)

- [3].A fast-locking bang-bang phase-locked loop with adaptive loop gain controller[J]. Journal of Semiconductors 2018(12)

- [4].CsPbBr_3 nanocrystal for mode-locking Tm-doped fiber laser[J]. Chinese Physics B 2019(09)

- [5].A Ka-band wide locking range frequency divider with high injection sensitivity[J]. Journal of Semiconductors 2014(03)

- [6].Novel homodyne frequency-shifting interference pattern locking system[J]. Chinese Optics Letters 2016(06)

- [7].Modulation-free laser frequency ofset locking using bufer gas-induced resonance[J]. Chinese Optics Letters 2013(10)

- [8].A comprehensive simulation of weak-light phase-locking for space-borne gravitational wave antenna[J]. Science China(Technological Sciences) 2016(05)

- [9].A wide locking range and low DC power injection-locked frequency tripler for K-band application[J]. Journal of Semiconductors 2014(12)

- [10].Low-power wide-locking-range injection-locked frequency divider for OFDM UWB systems[J]. 半导体学报 2009(05)

- [11].The role of nonlinearities associated with air-sea coupling processes in El Nino's peak-phase locking[J]. Science China(Earth Sciences) 2013(11)

- [12].A fast-locking all-digital delay-locked loop for phase/delay generation in an FPGA[J]. 半导体学报 2011(10)

- [13].Modified biplanar open-wedge high tibial osteotomy with rigid locking plate to treat varus knee[J]. Journal of Zhejiang University(Science B:An International Biomedicine，Biochemistry & Biotechnology Journal) 2009(09)

- [14].All-optical NOR gate based on injection-locking effect in a semiconductor laser[J]. Optoelectronics Letters 2008(01)

- [15].Carrier-envelope phase locking of 5 fs amplified Ti:sapphire laser pulse at 1 kHz repetition rate[J]. Chinese Science Bulletin 2008(05)

- [16].Ultrabroadband wavelength-swept source based on total mode-locking of an Yb:CaF_2 laser[J]. Photonics Research 2019(02)

- [17].Theoretic research on mutual injection phase-locking of four fiber lasers[J]. Optoelectronics Letters 2010(03)

- [18].Precise time frequency synchronization technology for bistatic radar[J]. Journal of Systems Engineering and Electronics 2008(05)

- [19].Laser frequency offset-locking using electromagnetically induced transparency spectroscopy of ~(85)Rb in magnetic field[J]. Chinese Physics B 2018(09)

- [20].Frequency locking of a 399-nm laser referenced to fluorescence spectrum of an ytterbium atomic beam[J]. Chinese Optics Letters 2014(02)

- [21].Numerical analysis of mode locking in multi-core photonic crystal fiber[J]. Chinese Science Bulletin 2010(18)

- [22].Volar locking distal radius plates show better short-term results than other treatment options: A prospective randomised controlled trial[J]. World Journal of Orthopedics 2016(10)

- [23].Passive harmonic mode locking of gain-guided solitons in erbium-doped fiber lasers[J]. Chinese Science Bulletin 2008(05)

- [24].Simulation and Analysis of Flexible Solar Panels' Deployment and Locking Processes[J]. Journal of Shanghai Jiaotong University(Science) 2008(03)

- [25].Frequency-locking and threshold current-lowering effects of a quantum cascade laser and an application in gas detection field[J]. Chinese Physics B 2015(02)

- [26].Hybrid phase-locked loop with fast locking time and low spur in a 0.18-μm CMOS process[J]. Chinese Physics B 2014(07)

- [27].Analysis of the relationship between deep venous catheter-related infection and post-operative complications in patients receiving minimally invasive esophagectomy[J]. Oncology and Translational Medicine 2020(02)

- [28].Deformation of the Haiyuan-Liupanshan fault zone inferred from the denser GPS observations[J]. Earthquake Science 2015(Z1)

- [29].Power-combining based on master-slave injection-locking magnetron[J]. Chinese Physics B 2016(07)

- [30].Unilateral self-locking mechanism for inchworm in-pipe robot[J]. Journal of Central South University of Technology 2010(05)

本文来源: https://www.lunwen90.cn/article/439cae8817bb6beff87a3f4f.html