# Development of pot-cover effect apparatus with freezing-thawing cycles

### 论文摘要

‘Pot-cover effect’ refers to the phenomenon of moisture accumulation beneath the pavement under condensation or desublimation because the vapor transfer in the soil is blocked by the pavement. To study this phenomenon in the laboratory, we have developed the pot-cover effect apparatus with freezing-thawing cycles（PEAFC）, which consists of three parts, namely, the vapor transfer system, the temperature control system, and the temperature and water content monitoring system. The major functions of this apparatus include: simulation of both vapor transfer and freezing-thawing cycling in the soil, real-time monitoring of the temperature and the water content in soil samples, and one-dimensional heat and moisture transfer in the samples. The FDR（frequency domain reflectometry） sensors of the apparatus are calibrated and a calibration formula is proposed to eliminate the water content measurement errors induced by temperature changes. Constant temperature difference tests and a freezing-thawing cycling test are conducted with the apparatus. Results indicate that the apparatus can control the water replenishment in the soil samples, monitor the vapor transfer in the samples in real time, and simulate the vapor transfer process under the condition of the freezing-thawing cycling in the soil. These tests verify the effectiveness and reliability of the apparatus, which indicates that the development purpose is achieved.

### 论文目录

### 文章来源

类型: 期刊论文

作者: LUO Ting,CHEN Han,YAO YangPing,WANG NaiDong,QU Xiao

来源: Science China(Technological Sciences) 2019年09期

年度: 2019

分类: 工程科技Ⅱ辑

专业: 公路与水路运输

单位: School of Transportation Science and Engineering, Beihang University

基金: supported by the National Program on Key Basic Research Project of China(Grant No.2014CB47006),the National Natural Science Foundation of China(Grant Nos.51579005&11272031)

分类号: U416.0

页码: 1636-1648

总页数: 13

文件大小: 1107K

下载量: 28

### 相关论文文献

- [1].On the determination and simulation of seawater freezing point temperature under high pressure[J]. Advances in Polar Science 2019(04)

- [2].Geotechnical problems on freezing ground soil and experimental investigation in Kazakhstan[J]. Sciences in Cold and Arid Regions 2017(03)

- [3].Field application of freezing technology for social infrastructures[J]. Sciences in Cold and Arid Regions 2015(05)

- [4].Influence of freezing rate on cryo-damage of cementitious material[J]. Journal of Zhejiang University(Science A:An International Applied Physics & Engineering Journal) 2009(01)

- [5].Numerical Simulation of Freezing Progress of Plasma[J]. 科技视界 2017(18)

- [6].Theoretical and numerical studies of crack initiation and propagation in rock masses under freezing pressure and far-field stress[J]. Journal of Rock Mechanics and Geotechnical Engineering 2014(05)

- [7].The Influence of Freezing Drizzle on Wire Icing during Freezing Fog Events[J]. Advances in Atmospheric Sciences 2013(04)

- [8].Dexamethasone prevents vascular damage in earlystage non-freezing cold injury of the sciatic nerve[J]. Neural Regeneration Research 2016(01)

- [9].肉类冷冻理论与冷冻新技术(英文) [J]. 肉类研究 2008(10)

- [10].Frost-heaving pressure in geotechnical engineering materials during freezing process[J]. International Journal of Mining Science and Technology 2018(02)

- [11].今天真冷![J]. 家教世界 2012(05)

- [12].Numerical simulation of artificial ground freezing in a fluid-saturated rock mass with account for filtration and mechanical processes[J]. Sciences in Cold and Arid Regions 2017(04)

- [13].The migration and transformation of dissolved organic matter during the freezing processes of water[J]. Journal of Environmental Sciences 2015(01)

- [14].Exact analytical solution to three-dimensional phase change heat transfer problems in biological tissues subject to freezing[J]. Applied Mathematics and Mechanics(English Edition) 2009(01)

- [15].Soil freezing process and different expressions for the soil-freezing characteristic curve[J]. Sciences in Cold and Arid Regions 2017(03)

- [16].Different discretization method used in coupled water and heat transport mode for soil under freezing conditions[J]. Sciences in Cold and Arid Regions 2013(04)

- [17].Experimental study on freezing of liquids under static magnetic field[J]. Chinese Journal of Chemical Engineering 2017(09)

- [18].Sessile droplet freezing and ice adhesion on aluminum with different surface wettability and surface temperature[J]. Science China(Physics,Mechanics & Astronomy) 2015(07)

- [19].Numerical study on freezing-thawing phase change heat transfer in biological tissue embedded with two cryoprobes[J]. Journal of Central South University of Technology 2009(02)

- [20].Compressibility of fine-grained soils subjected to closed-system freezing and thaw consolidation[J]. Mining Science and Technology 2009(05)

- [21].Coupling microchip electrophoresis with MALDI-TOF-MS based on a freezing technique[J]. Chinese Chemical Letters 2013(06)

- [22].Controlled Freezing and Open-Pulled Straw (OPS) Vitrification of In vitro Produced Bovine Blastocysts FollowingAnalysis of ATP Content and Reactive Oxygen Species (ROS) Level[J]. Journal of Integrative Agriculture 2012(03)

- [23].Combination effect of seasonal freezing and artificial freezing on frost heave of silty clay[J]. Journal of Central South University of Technology 2010(01)

- [24].Sampling duration and freezing temperature influence the analysed gastric inositol phosphate composition of pigs fed diets with different levels of phytase[J]. Animal Nutrition 2019(02)

- [25].Experimental investigations of freezing soils at ground conditions of Astana, Kazakhstan[J]. Sciences in Cold and Arid Regions 2015(04)

- [26].Study of the insulation effect of freezing apparatuses[J]. Sciences in Cold and Arid Regions 2012(01)

- [27].Study on the freezing–thawing deformation of consolidated soils under high pressure[J]. Sciences in Cold and Arid Regions 2017(01)

- [28].Effect of intensity and duration of freezing on soil microbial biomass, extractable C and N pools, and N_2O and CO_2 emissions from forest soils in cold temperate region[J]. Science China(Earth Sciences) 2016(01)

- [29].Farinose fiavonoids are associated with high freezing tolerance in fairy primrose (Primula malacoides) plants[J]. Journal of Integrative Plant Biology 2014(02)

- [30].Application of Colligative Properties in Quality Detection of Watering Raw Milk[J]. Animal Husbandry and Feed Science 2011(02)

本文来源: https://www.lunwen90.cn/article/592c024376ea2c95923eaa39.html