# Anion intercalated layered-double-hydroxide structure for efficient photocatalytic NO remove

### 论文摘要

Due to the easily controllable interlayer anions, metal cation composition proportion and thickness, which is beneficial to modify surface chemical state and tune bandgap, layered double hydroxides（LDHs） have great promising potential for photocatalytic applications. In this study,we have successfully synthesized the ZnAl–LDH intercalated the single anion between ZnAl cationic interlayer without anionic impurities by using a facile calcining and reconstructing routes. The electron structure and surface chemical state of the prepared products have been investigated by combining the DFT calculation and experimental characterization methods. UV–vis DRS was used to certify the light absorption of the prepared products, and we performed the DFT calculation to demonstrate the density of state and activation of reactant. These results suggested that the ZnAl–LDH–CO3 possessed the more proper band structure and superior ability to activate NO and O2 for accelerating the photocatalytic NO oxidation activity. Moreover, the in situ DRIFTS with dynamically monitoring intermediates and products over the ZnAl–LDH–CO3 was adopted to declare the photocatalytic NO oxidized process during the photocatalytic reaction process. This work illustrated the influence of different interlayer anions to the electron structure and surface chemical state of ZnAl–LDH structure through the experimental verification combined DFT calculation and the photocatalytic NO oxidized process via in situ DRIFTS analyzing, which would provide a novel way to design and fabricate the efficient photocatalysis, and understand the reaction process.

### 论文目录

### 文章来源

类型: 期刊论文

作者: Wangchen Huo,Tong Cao,Xiaoying Liu,Weina Xu,Biqin Dong,Yuxin Zhang,Fan Dong

来源: Green Energy & Environment 2019年03期

年度: 2019

分类: 工程科技Ⅱ辑,工程科技Ⅰ辑

专业: 环境科学与资源利用

单位: State Key Laboratory of Mechanical Transmissions, College of Materials Science and Engineering, Chongqing University,Engineering Research Center for Waste Oil Recovery Technology and Equipment, Ministry of Education, College of Environment and Resources, Chongqing Technology and Business University,College of Physics, Chongqing University,Guangdong Provincial Key Laboratory of Durability for Marine Civil Engineering, Shenzhen University,Research Center for Environmental Science & Technology, Institute of Fundamental and Frontier Sciences, University of Electronic Science and Technology of China

基金: financial support of the Fundamental Research Funds for the Central Universities (2018CDYJSY0055,106112017CDJXSYY0001,106112017C DJQJ138802,106112017CDJXSYY0001,106112017CDJS K04XK11,and 2018CDQYCL0027),the National Natural Science Foundation of China (Grant no. 21576034),the Innovative Research Team of Chongqing (CXTDG201602014),Project funded by Chongqing Special Postdoctoral Science Foundation (XmT2018043),Technological projects of Chongqing Municipal Education Commission (KJZDK201800801)

分类号: X701

页码: 270-277

总页数: 8

文件大小: 1258K

下载量: 9

### 相关论文文献

- [1].Mineralogical characteristics and photocatalytic properties of natural sphalerite from China[J]. Journal of Environmental Sciences 2020(03)

- [2].Direct photocatalytic CH_4 oxidation to oxygenates with O_2 at room temperature in water[J]. Science Foundation in China 2020(01)

- [3].Functional groups to modify g-C_3N_4 for improved photocatalytic activity of hydrogen evolution from water splitting[J]. Chinese Chemical Letters 2020(06)

- [4].A new phosphidation route for the synthesis of NiP_x and their cocatalytic performances for photocatalytic hydrogen evolution over g-C_3N_4[J]. Journal of Energy Chemistry 2020(09)

- [5].Rational design of multinary copper chalcogenide nanocrystals for photocatalytic hydrogen evolution[J]. Journal of Semiconductors 2020(09)

- [6].Preparation and photocatalytic performance of ZnO/ZnGa_2O_4 composite microspheres[J]. Journal of Central South University 2016(12)

- [7].Solar photocatalytic energy conversion[J]. Science Bulletin 2017(09)

- [8].Enhanced photocatalytic hydrogen evolution along with byproducts suppressing over Z-scheme Cd_xZn_(1-x)S/Au/g-C_3N_4 photocatalysts under visible light[J]. Science Bulletin 2017(09)

- [9].TiO_2-based materials for photocatalytic hydrogen production[J]. Journal of Energy Chemistry 2017(02)

- [10].Preparation,characterization and photocatalytic properties of BiOBr/ZnO composites[J]. Journal of Energy Chemistry 2017(03)

- [11].Oxygen-rich carbon-nitrogen quantum dots as cocatalysts for enhanced photocatalytic H_2 production activity of TiO_2 nanofibers[J]. Progress in Natural Science:Materials International 2017(03)

- [12].Dysprosium cerate nanostructures:facile synthesis,characterization,optical and photocatalytic properties[J]. Journal of Rare Earths 2017(08)

- [13].Facile synthesis of Cu/tetrapod-like ZnO whisker compounds with enhanced photocatalytic properties[J]. Journal of Semiconductors 2017(09)

- [14].Enhancement of photocatalytic efficiency by in situ fabrication of BiOBr/BiVO_4 surface junctions[J]. Journal of Environmental Sciences 2017(10)

- [15].La/Ce-codoped Bi_2O_3 composite photocatalysts with high photocatalytic performance in removal of high concentration dye[J]. Journal of Environmental Sciences 2017(10)

- [16].Morphology dependent photocatalytic activity of WO_3 nanostructures[J]. Journal of Energy Chemistry 2015(02)

- [17].A review on 2D MoS_2 cocatalysts in photocatalytic H_2 production[J]. Journal of Materials Science & Technology 2020(21)

- [18].CdS nanosheets decorated with Ni@graphene core-shell cocatalyst for superior photocatalytic H_2 production[J]. Journal of Materials Science & Technology 2020(21)

- [19].Liquid exfoliating CdS and MoS_2 to construct 2D/2D MoS_2/CdS heterojunctions with significantly boosted photocatalytic H_2 evolution activity[J]. Journal of Materials Science & Technology 2020(21)

- [20].Construction 0D TiO_2 nanoparticles/2D CoP nanosheets heterojunctions for enhanced photocatalytic H_2 evolution activity[J]. Journal of Materials Science & Technology 2020(21)

- [21].Identifying the active photocatalytic H_2-production sites on TiO_2-supported Pt nanoparticles by the in-situ infrared spectrum of CO[J]. Science China(Chemistry) 2020(03)

- [22].Preparation and photocatalytic activity of Fe_3O_4@SiO_2@ZnO:La[J]. Journal of Rare Earths 2020(12)

- [23].Visible light photocatalytic dye decomposition behaviour of solid state reaction grown Zn_2TiO_4 nanoparticles[J]. Journal of Semiconductors 2018(12)

- [24].Effect of doping of different rare earth(europium,gadolinium,dysprosium and neodymium) metal ions on structural,optical and photocatalytic properties of LaFeO_3 perovskites[J]. Journal of Rare Earths 2019(12)

- [25].Construction of one dimensional ZnWO_4@SnWO_4 core-shell heterostructure for boosted photocatalytic performance[J]. Journal of Materials Science & Technology 2019(10)

- [26].Recent advances based on the synergetic effect of adsorption for removal of dyes from waste water using photocatalytic process[J]. Journal of Environmental Sciences 2018(03)

- [27].Enhanced photocatalytic performance of carbon quantum dots/Bi OBr composite and mechanism investigation[J]. Chinese Chemical Letters 2018(06)

- [28].Designing all-solid-state Z-Scheme 2D g-C_3N_4/Bi_2WO_6 for improved photocatalysis and photocatalytic mechanism insight[J]. Green Energy & Environment 2018(03)

- [29].Flower-like Au/Ag/TiO_2 nanocomposites with enhanced photocatalytic efficiency under visible light irradiation[J]. Science China(Chemistry) 2017(04)

- [30].Carbon-nanodot-coverage-dependent photocatalytic performance of carbon nanodot/TiO_2 nanocomposites under visible light[J]. Chinese Physics B 2017(05)

本文来源: https://www.lunwen90.cn/article/85d423eeb65e1e42316f2897.html