# Oncell触摸屏工艺Bubble的分析与改善研究

### 论文摘要

通过对Oncell触摸屏工艺(TSP)Bubble的定性分析与产生机理研究,发现液晶扩散不足和玻璃基板形变量大是不良产生的直接原因,并分别从产品设计、工艺参数、材料性能等方面进行改善性研究。实验结果表明:1)在产品设计上优化液晶滴下位置和框胶与聚酰亚胺配向膜间距;2)在工艺参数上管控真空贴合保持时间和ODF产出到TSP投入的间隔时间;3)在材料性能上提升玻璃基板厚度和框胶粘合力等,均有利于TSP Bubble不良的改善,最终TSP Bubble的不良发生率由最初的68%降低到0.1%以下。

### 论文目录

- 引 言

- 1 TSP Bubble不良的定性分析

- 2 TSP Bubble不良的机理分析

- 2.1 液晶扩散

- 2.2 玻璃基板形变

- 3 实验验证与结果讨论

- 3.1 产品设计

- 3.1.1 液晶滴下位置的优化

- 3.1.2 框胶与PI配向膜间距的优化

- 3.2 工艺参数

- 3.2.1 真空贴合保持时间的影响

- 3.2.2 ODF～TSP间隔时间的影响

- 3.3 材料性能

- 4 结 论

### 文章来源

类型: 期刊论文

作者: 王立苗,杨小飞,李兴华,樊浩原,刘旭,牟勋,杨慧光,张正东,郭明周

关键词: 液晶显示屏,气泡,触摸屏工艺,扩散,形变

来源: 光电子技术 2019年04期

年度: 2019

分类: 信息科技

专业: 电信技术

单位: 成都京东方光电科技有限公司,绵阳京东方光电科技有限公司

分类号: TN873.93

DOI: 10.19453/j.cnki.1005-488x.2019.04.011

页码: 275-278

总页数: 4

文件大小: 1223K

下载量: 63

### 相关论文文献

- [1].Theoretical estimation of sonochemical yield in bubble cluster in acoustic field[J]. Chinese Physics B 2020(01)

- [2].Scaling of the bubble/slug length of Taylor flow in a meandering microchannel[J]. Chinese Journal of Chemical Engineering 2019(11)

- [3].Modeling bubble column reactor with the volume of fluid approach:Comparison of surface tension models[J]. Chinese Journal of Chemical Engineering 2019(11)

- [4].Interaction of two in-line bubbles of equal size rising in viscous liquid[J]. Chinese Journal of Chemical Engineering 2020(01)

- [5].Phase field simulation of single bubble behavior under an electric field[J]. Chinese Physics B 2018(09)

- [6].Three-dimensional measurement of bubble volume based on dual perspective imaging[J]. Optoelectronics Letters 2017(01)

- [7].Effect of wall jet on the bubble dynamics near arigid wall[J]. 排灌机械工程学报 2017(06)

- [8].Theoretical analysis of interaction between a particle and an oscillating bubble driven by ultrasound waves in liquid[J]. Chinese Physics B 2017(11)

- [9].Analysis on the factors that influence bubble coalescence in an acoustic field[J]. Chinese Journal of Acoustics 2016(01)

- [10].TFT-LCD制程中Bubble的分析与改善研究[J]. 电子技术与软件工程 2015(11)

- [11].A simple approach for bubble modelling from multiphase fluid simulation[J]. Computational Visual Media 2015(02)

- [12].Performance evaluation of a bubble generator and a bubble separator designed for the gas removal system of a small thorium molten salt reactor[J]. Chinese Journal of Chemical Engineering 2020(05)

- [13].Multi-bubble motion behavior of electric field based on phase field model[J]. Chinese Physics B 2019(03)

- [14].Numerical analysis of the interaction of 3D compressible bubble clusters[J]. Applied Mathematics and Mechanics(English Edition) 2019(08)

- [15].CFD simulation of gas–liquid flow in a high-pressure bubble column with a modified population balance model[J]. Chinese Journal of Chemical Engineering 2018(06)

- [16].Numerical simulation of motion and deformation of ring bubble along body surface[J]. Applied Mathematics and Mechanics(English Edition) 2013(12)

- [17].Interaction of a bubble and a bubble cluster in an ultrasonic field[J]. Chinese Physics B 2013(01)

- [18].Effects of surface tension on bubble growth in an extensive uniformly superheated liquid[J]. Chinese Science Bulletin 2011(30)

- [19].Numerical simulation of bubble breakup phenomena in anarrow flow field[J]. Applied Mathematics and Mechanics(English Edition) 2010(04)

- [20].Comparison between the 3D numerical simulation and experiment of the bubble near different boundaries[J]. Science in China(Series G:Physics,Mechanics & Astronomy) 2008(12)

- [21].Thirst for Bubble Tea[J]. Beijing Review 2019(51)

- [22].创意冰箱U-Bubble[J]. 发明与创新(中学生) 2015(12)

- [23].INTERACTION OF A CAVITATION BUBBLE AND AN AIR BUBBLE WITH A RIGID BOUNDARY[J]. Journal of Hydrodynamics 2010(04)

- [24].Comparison of Xe single bubble sonoluminescence in water and sulfuric acid[J]. Chinese Physics B 2008(08)

- [25].Interaction of underwater explosion bubble with complex elastic-plastic structure[J]. Applied Mathematics and Mechanics(English Edition) 2008(01)

- [26].Characteristics of a bubble jet near a vertical wall[J]. Journal of Marine Science and Application 2008(01)

- [27].Pulse chirping effect on controlling the transverse cavity oscillations in nonlinear bubble regime[J]. Chinese Physics B 2017(02)

- [28].中国/BUBBLE智能桌面机器人[J]. 设计 2017(02)

- [29].爱上堆积色彩的感觉 宅男带你体验手游《Bubble Bust》[J]. 电脑爱好者(普及版) 2011(11)

- [30].3D reconstruction of single rising bubble in water using digital image processing and characteristic matrix[J]. Particuology 2013(02)

本文来源: https://www.lunwen90.cn/article/95b11099e65c2bf239416b5f.html