# Velocity and Temperature of In-Flight Particles and Its Significance in Determining the Microstructure and Mechanical Properties of TBCs

### 论文摘要

The correlation between particle in-flight parameter, defect content and mechanical property of yttria-stabilized zirconia coating was systematically studied in the present work. The melting state of in-flight particle during spraying was simulated using computational fluid dynamics. The results suggested that, with the increase of velocity and temperature of in-flight particles in the plasma jet, the particles changed from partially melted state to fully melted one. As a result, the total defect content of as-sprayed coating gradually decreased, while elastic modulus and microhardness increased correspondingly. However, the fracture toughness of as-sprayed coating reached a maximum value when the total defect content reached approximately 9.1%.

### 论文目录

- 1 Introduction

- 2 Experimental

- 2.1 Materials

- 2.2 Plasma Spraying Process

- 2.3 Interaction Between Plasma Jet and In-Flight Particles

- 2.4 Specimen Characterization

- 2.5 Microhardness and Weibull Analysis

- 3 Results and Discussion

- 3.1 Analysis of Plasma Jet and Melting State of In-Flight Particles

- 3.2 Microstructure of As-Sprayed Coating

- 3.3 Microhardness and Weibull Plots

- 3.4 Elastic Modulus and Fracture Toughness

- 4 Conclusions

### 文章来源

类型: 期刊论文

作者: Lei Zhang,Tao He,Yu Bai,Fang-Li Yu,Wei Fan,Yu-Shan Ma,Zhan-Dong Chang,Hai-Bo Liu,Ben-Qiang Li

来源: Acta Metallurgica Sinica(English Letters) 2019年10期

年度: 2019

分类: 工程科技Ⅰ辑,工程科技Ⅱ辑

专业: 金属学及金属工艺,动力工程

单位: State Key Laboratory for Mechanical Behavior of Materials,Xi'an Jiaotong University,Wuzhong Instrument Co. Ltd,School of Materials Engineering,Xi'an Aeronautical University,Department of Mechanical Engineering,University of Michigan

基金: supported by the Collaborative Innovation Center of Advanced Control Valve Project (Grant No. WZYB-XTCX-001)

分类号: TG174.4;TK471

页码: 1269-1280

总页数: 12

文件大小: 10129K

下载量: 3

### 相关论文文献

- [1].Microstructure and microhardness of a novel TiZrAlV alloy by laser gas nitriding at different laser powers[J]. Rare Metals 2020(03)

- [2].Statistical Characteristics of Microhardness of Hardened Cement Paste[J]. Journal of Wuhan University of Technology(Materials Science) 2018(04)

- [3].Dendritic morphology evolution and microhardness enhancement of rapidly solidified Ni-based superalloys[J]. Science China(Technological Sciences) 2019(11)

- [4].Microstructure and microhardness of Ti-48Al alloy prepared by rapid solidification[J]. China Foundry 2020(06)

- [5].Effect of growth rate on microstructure and microhardness of directionally solidified Ti-44Al-5Nb-1.5Cr-1.5Zr-1Mo-0.1B alloy[J]. China Foundry 2020(04)

- [6].Fabrication and wear properties of co-deposited Ni-Cr nanocomposite coatings[J]. Transactions of Nonferrous Metals Society of China 2010(01)

- [7].Properties of nanocrystalline copper prepared by vacuum-warm-compaction method[J]. Transactions of Nonferrous Metals Society of China 2009(02)

- [8].Effect of Ti Addition on the Microstructure and Property of FeAlCuCrNiMo_(0.6) High-Entropy Alloy[J]. Acta Metallurgica Sinica(English Letters) 2020(07)

- [9].Microstructure Evolution and Microhardness of Ultrafine-grained High Carbon Steel during Multiple Laser Shock Processing[J]. Journal of Iron and Steel Research(International) 2015(01)

- [10].Microstructure and microhardness of nanostructured Al-4.6Cu-Mn alloy ribbons[J]. International Journal of Minerals Metallurgy and Materials 2015(08)

- [11].Indentation size effect in microhardness measurements of Hg_(1-x)Mn_xTe[J]. Transactions of Nonferrous Metals Society of China 2009(S3)

- [12].Selective Laser Melting of In Situ TiB/Ti6Al4V Composites: Formability, Microstructure Evolution and Mechanical Performance[J]. Acta Metallurgica Sinica(English Letters) 2020(06)

- [13].Magnetocaloric properties,microhardness and corrosion resistance of Gd_(100–x)Zr_x alloys[J]. Journal of Rare Earths 2016(09)

- [14].Effect of Aging Treatment on Microstructural and Mechanical Characteristics of PEO Coatings on Mg-Al Alloy[J]. Journal of Materials Science & Technology 2008(01)

- [15].Study on characteristics of Ni-W-B composites containing CeO_2 nano-particles prepared by pulse electrodeposition[J]. Journal of Rare Earths 2012(01)

- [16].Microhardness,Microstructure and Electrochemical Efficiency of an Al(Zn/xMg) Alloy after Thermal Treatment[J]. Journal of Materials Science & Technology 2012(03)

- [17].Influence of processing temperature on microstructure and microhardness of copper subjected to high-pressure torsion[J]. Science China(Technological Sciences) 2010(06)

- [18].Corrosion Resistance of Friction Stir Welded Al–Cu–Li Alloy AA2099-T8[J]. Acta Metallurgica Sinica(English Letters) 2020(01)

- [19].Enhancing Wear Resistance of A356 Alloy by Adding CNFs Based on Ultrasonic Vibration Casting[J]. Acta Metallurgica Sinica(English Letters) 2018(05)

- [20].Mechanical Properties of Vermicular Graphite Cast Iron Processed by Selective Laser Surface Alloying with Ultra-fine ZrO_2 Ceramic Particulates[J]. Acta Metallurgica Sinica(English Letters) 2016(11)

- [21].Influence of Three Remineralization Materials on Physicochemical Structure of Demineralized Enamel[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2014(02)

- [22].Coarsening and Age Hardening Behaviors of γ' Particles in GH742 During High Temperature Treatment[J]. Journal of Iron and Steel Research(International) 2009(05)

- [23].Characterizations of precipitation behavior of Al-Mg-Si alloys under different heat treatments[J]. China Foundry 2018(02)

- [24].Surface Nanocrystallization of Steel 20 Induced by Fast Multiple Rotation Rolling[J]. Journal of Harbin Institute of Technology 2015(05)

- [25].Hydrothermal growth of Ni-based coatings on copper substrates[J]. International Journal of Minerals Metallurgy and Materials 2012(03)

- [26].Microstructure and Hardness of Laser Shocked Ultra-fine-grained Aluminum[J]. Journal of Materials Science & Technology 2011(09)

- [27].Surface Nanocrystallization of Magnesium Alloy AZ91D by High-Energy Shot Peening[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2009(04)

- [28].Microstructure and properties of TiN/Ni composite coating prepared by plasma transferred arc scanning process[J]. Transactions of Nonferrous Metals Society of China 2009(05)

- [29].A Novel Method for Achieving Gradient Microstructure in a Cu-Al Alloy:Surface Spinning Strengthening (3S)[J]. Acta Metallurgica Sinica(English Letters) 2017(03)

- [30].Improved mechanical properties of Ni-rich Ni_3Al coatings produced by EB-PVD for repairing single crystal blades[J]. Rare Metals 2017(07)

本文来源: https://www.lunwen90.cn/article/be3b77ba775d4a6fe306b4a3.html